## Slide 1: Advanced x86: BIOS and System Management Mode Internals System Management Mode (SMM)
Xeno Kovah && Corey Kallenberg
LegbaCore, LLC

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”

## Slide 3: System Management Mode (SMM)
God Mode Activate

## Slide 4
From http://support.amd.com/us/Processor_TechDocs/24593.pdf
Batteries Not
Included!
Notes: http://www.explore-science-fiction-movies.com/images/fix-its-batteries-not-included-nest.jpg

## Slide 5: System Management Mode (SMM) Overview
Most privileged x86 processor operating mode
Runs transparent to the operating system
When the processor enters SMM, all other running tasks are suspended
SMM can be invoked only by a System Management Interrupt (SMI) and exited only by the RSM (resume) instruction
Intended use is to provide an isolated operating environment for
  Power/Battery management
  Controlling system hardware
  Running proprietary OEM code
  etc. (anything that should run privileged and uninterrupted)

## Slide 6: System Management Mode (SMM) Overview
The code that executes in SMM (called the SMI handler) is instantiated from the BIOS flash
Protecting SMM is a matter of protecting both the active (running) SMRAM address space but also protecting the flash chip from which it is derived
  Protect itself (SMBASE (location), SMRAM Permissions)
  Write-Protect Flash
So far in our research, only about 5% of SMRAM configurations were directly unlocked and vulnerable to overwrite
However, since > 50% of the BIOS flash chips we've seen are vulnerable, that means > 50% of SMRAM will follow suit

## Slide 7: System Management Interrupt (SMI)
SMM can only be invoked by signaling a System Management Interrupt (SMI)
SMI’s can be received via the SMI# pin on the processor or through the APIC bus
SMI’s cannot be masked like normal interrupts (e.g. with the “cli” instruction, or clearing the IF bit in EFLAGS)
SMI’s are independent from the normal processor interrupt and exception-handling mechanisms
SMI’s take precedence over non-maskable and maskable interrupts
  Including debug exceptions and external interrupts
If a SMI and NMI occur at the same time, only the SMI will be handled

## Slide 8: Causes of SMI#
Just an example, your ICH/PCH will list them for your system
Notes: SCI are interrupts for ACPI, not part of this class

## Slide 9: Generating SMI: APM
This is applicable to systems that support Advanced Power Management (most do these days)
Fixed I/O range, so it cannot be relocated
Check your I/O Controller Hub datasheet to verify its supported
Writes to 0xB3 do not trigger an SMI#, only the write to 0xB2
0xB3 can be used to pass information

## Slide 10: Advanced Power Management (APM)
APM_CNT (0xB2) is the control register
APM_STS (0xB3) is the status register
Located in I/O Address space
Registers are R/W
Note: APM != ACPI, but even on other systems which use ACPI 2.0, this still triggers an SMI#
  The PCH datasheets (up to 8-series) also still list these under the fixed IO address
Notes: Check PCH and include location, if different, otherwise note its static location. Its in LPC so it should be the same

## Slide 11: APM_CNT & APM_STS
Writing a byte to port 0xB2 will trigger an SMI#
Writing to 0xB3 does NOT trigger SMI#
Can be used to pass information to the SMI handler.
Control flow through the SMI handler can be determined by the values in ports B2 & B3h
Usage: Could tell the SMI handler to measure Hypervisor memory, or initiate a BIOS update

## Slide 12: Examples
OUT 0xB2, 0x12
MOV DX, 0x1234
OUT 0xB2, DX
OUT 0xB3, 0x34
OUT 0xB2, 0x12
Generates SMI. SMI handler can read port 0xB2 to see that 0x12 was passed.
Writes 0x34 to 0xB3 and 0x12 to 0xB2 all in one shot (Generating SMI).
Writes 0x34 to 0xB3 and then writes 0x12 to 0xB2. SMI is triggered only on the write to 0xB2.

## Slide 13: Generating SMI via APIC
  We've not yet had time to play with this
  Should be able to generate SMI by programming the Interrupt Command Register in the APIC
  Architecture (and APIC type) dependent
  There is also a Self IPI register

## Slide 14: “Corollary” SMI# generation
Looking through the datasheets there are various (too many to show) register/bit-combinations that will also generate an SMI
John called this a “corollary” SMI#. The SMI# is correlated with software is setting a register bit

## Slide 15: SMI invocation example
  Open a port IO window in RW-E at address 0xB2
  Type in the number 1 and hit enter
    I choose 1 because I know it to be a ‘safe’ value to enter
  Notice anything?
    (You’re not supposed to)
  The system just transitioned into SMM, executed code, and then exited SMM

## Slide 16: SMI invocation counter
  So we’ve seen that there are a lot of events that can generate SMI and we’ve generated some on our own as well
  One logical question is: how frequently are these generated?
  As always, the answer is “it depends”
  On a system like a laptop, SMM will likely be called frequently to check the battery/power status
    Should be an SMI# in that case
  But on a desktop it may be called much less frequently

## Slide 17: SMI counter (MSR)
  And as if answering my wishes for some way to track how frequently SMM is entered, I found this in Intel’s Software Programming Guide (Chapter 35, MSRs)
  It’s only available on Nehalem and later processor families (new stuff)
  Trying to read this will crash any system that doesn’t support it
    I hope you read this before trying ;)
Nehalem (Core i series & Xeon) and later architectures only!
From Intel Vol. 3. Ch. "Model Specific Registers (MSRs)"

## Slide 18: Periodic SMI#
  More as a side note (but related to the SMI counter), SMI# can be configured to fire periodically
  This way it can be guaranteed that SMI will be generated at least once every 8, 16, 32, or 64 seconds
  This register is R/W and resides on the LPC bus (D31:F0, offset A0h, bits 1:0)

## Slide 20: Reversing tip: searching for SMI communication byte patterns
  You can search for instances where a program is communicating with SMM via port IO by searching for byte patterns like those above
  To locate triggering of SMI via port 0xB2, you can search for the bytes “E6 B2” and “E7 B2” in IDA Pro
    Single byte searches for EE and EF yield many false-positives so analyze the code before it to ensure that the DX register contains B2
  You can also script IDA to create IDB files for all binaries in a folder, and then search within those binaries for “out 0B2h,”
From Intel Vol. 2

## Slide 21: SMI byte patterns example
  Searching for instances of “E6 B2” and “E7 B2” in IDA will yield a list of examples like that on the left
  Most importantly, IDA provides an interesting clue here to a problem that we’ll be covering shortly…
  And is actually the only reason this slide is included

## Slide 22: Entering SMM
When receiving an SMI, the processor waits for all instructions to complete and stores to complete
SMI interrupts are handled on an architecturally defined “interruptible” point in program execution
  Like an instruction boundary:
XOR EAX, EAX
ADD EAX, 1
Architecturally “interruptible” point
Processor saves the context in SMRAM and begins executing the SMI Handler
In a multi-core processor, no SMI handler code is executed until all cores have performed the above and entered SMM

## Slide 23: Entering SMM due to IO
IO Instruction restart field is located in the state save area in SMRAM
  SMBASE + 8000 + 7F00h
If an IO instruction to a device triggers an SMI, the SMI handler has the option of re-executing that instruction upon returning from SMM
  Example: If a device is asleep, port IO to it may generate SMI#. The SMI handler can then wake up the device and re-execute the instruction that generated the original SMI#
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 24: Exiting SMM: RSM
The only way to exit SMM is through the RSM instruction
  Or system reset/shut down
Returns control to the application program or operating-system procedure that was interrupted by the SMI
The processor’s state is restored from the save state area within SMRAM. If the processor detects invalid state information during state restoration, it enters the shutdown state.
The operating mode the processor was in at the time of the SMI is restored.
RSM can only be executed from within SMM
  So if you see this, you are debugging the SMRAM code
  RSM multi-byte opcode is: 0x0F 0xAA
Executing RSM while not in SMRAM generates an invalid opcode exception
From Intel Vol. 2

## Slide 25: “Performance Implications of System Management Mode”
Here’s a good paper which pushes back against all the academic researchers who act like they can just implement all their security features in SMM
http://web.cecs.pdx.edu/~karavan/research/SMM_IISWC_preprint.pdf

## Slide 26: “Performance Implications of System Management Mode” 2