## Slide 1: Advanced x86: BIOS and System Management Mode Internals
John Butterworth & Xeno Kovah
Part 1

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ’Introductory Intel x86: Assembly, Architecture, and Applications’ class"

## Slide 3
You are here!
Welcome x86 Machine Masters!!!

## Slide 4
Intermediate x86
2 day, Xeno Kovah
Advanced x86:
Virtualization
2 day, David Weinstein
Intro x86-64
2 day, Sam Cornwell
Life of Binaries
2 day, Xeno Kovah
Stealth Malware
2 day, Xeno Kovah
Required
Recommended
Approved
Intended Future
r0x0r Skill Tree
"PC deep system security & trusted computing"
Advanced x86:
BIOS & SMM (System Management Mode)
2 day, John Butterworth
Intro Trusted Computing
2 day, Ariel Segall
Advanced x86:
Trusted Execution Technology (TXT)
2 day, Xeno Kovah
Intel SGX
2 day, Xeno Kovah
YOU ARE HERE

## Slide 5: About Us
Full time security researchers at The MITRE Corporation
"The author's affiliation with The MITRE Corporation is provided for identification purposes only, and is not intended to convey or imply MITRE's concurrence with, or support for, the positions, opinions or viewpoints expressed by the author."
Officially here as LegbaCore, LLC, our training company
  "Papa Legba, Hear my call!"
We've never been employed as BIOS developers, we've just just been researchers investigating what it would take to build more secure systems
Notes: Papa Legba Hear My Call!
http://upload.wikimedia.org/wikipedia/commons/6/69/PapaLegbaCharlesSanderson.jpg

## Slide 6: About You
What is your name?
(What do you want/hope
to get out of the class?)
What is your department?
Have you taken, or did you review, Intro & Intermediate x86 per the class prereqs? ;)
  How often do you deal with x86 asm?
  How often do you deal with x86 architecture? (e.g. memory management, MSRs, control regs, etc)
  How often do you look at Intel manuals?
Did you review Intro to Reverse Engineering?
Do you prefer more lab time or more lecture time?
  I.e. do you want to understand fewer things through hands on experience, or want an infodump of all the stuff I know for you to sift through?
Notes: http://www.adventureclassicgaming.com/index.php/gallery/image/328/
http://www.adventureclassicgaming.com/images/galleries/54/54_6.jpg

## Slide 7: The work that led to this
Originally this work came about because we were using “Timing-Based Attestation” (TBA) research to build more trustworthy code in the Windows kernel, such as code looking for rootkits:
  http://www.ieee-security.org/TC/SP2012/papers/4681a239.pdf
At which point we thought it might be a good idea to apply the same principles of TBA to the system BIOS to ensure trustworthy firmware
  http://dl.acm.org/citation.cfm?id=2516714
Along the way to completing this we learned a lot about how the system works at the lowest level, where the problems lie.
And we've worked with BIOS vendors to help fix their problems and make more secure systems for everyone
This class comprises of the results of our findings

## Slide 8: This Course
Show you how to detect if a BIOS is vulnerable
Show you what an attacker can do as a result
Show you how it should be locked down
  Some things you can lock yourself, but for the most part it’s really the OEM who should be doing this
This course is not intended to be a complete discussion of BIOS and how it works
  Our goal is to fill-in concepts needed to understand the security
  There are other excellent sources for complete BIOS coverage:
  Darmawan Salihun*:
    http://bioshacking.blogspot.com/
    https://sites.google.com/site/pinczakko/home
    And his articles on http://resources.infosecinstitute.com/
  Anders at Techstream Inc. also offers a detailed course on BIOS/UEFI (www.techstream.com)
* Darmawan also covers security topics. He is working on a new book that should be ready in a year or so.
Notes: https://www-ssl.intel.com/content/www/us/en/processors/core/CoreTechnicalResources.html

## Slide 9: Course Outline
Introduction
Chipset basics
  How to identify a chipset
Boot process Overview
Entry vector & BIOS Operating Environment
Memory Map
I/O
  Memory-mapped IO
  Port IO
  PCI
  PCI Option ROMs
System Management Mode (SMM)
BIOS Flash (Serial Peripheral Interface (SPI), mostly)
Trusted Computing Technologies (TPM)
Introduction to UEFI
  Forensic analysis of UEFI BIOS
  Secure Boot
If you extrapolate well you will also learn how to write tools to do your own measuring ;)

## Slide 10: Course Goals
Provide you a basic background in BIOS technologies
  Some people already know a lot, others know less than zero.
  We’ll cover only the minimum required to understand the subsequent topic(s)
Convince you that having unlocked BIOS is a really bad thing that can adversely affect the entire system during runtime
Show you how to measure and interpret the results to understand if and how a system BIOS may be vulnerable
  Provide you a lot of hands-on examples when possible so you can “see” the effects
  Its such an abstract topic that provides very little visibility, I have sought to lift this veil
Convince you that this problem IS solvable! Especially the information which we cover over these 2 days
Introduce you to some forensics tools that can not only help you analyze and interpret whether a system BIOS is vulnerable, but also introduce you to some methods to analyze changes if you think a BIOS has been compromised
  There is still a lot of work to be done on the latter
Hopefully I have made this topic enjoyable. It’s easy for BIOS to be a snooze-fest, but we had fun creating portions of this and we hope it manifests itself

## Slide 11: Why Hack the BIOS?
Why would someone want to hack the BIOS?
  Because few organizations, if any, are checking the BIOS
  If you get a foothold there, it’s likely to be there for years
  Low level code initializes the system so the lower the attacker goes the further up the malware food chain he is
Is hacking the BIOS itself the end-goal?
  Likely not, it’s a stepping stone to get into SMM or some other portion of the system
  And to keep the foothold for years and years
  Likely one target will be SMM, since this provides the attacker nigh-maximum privileges (aka "God Mode" ;)), but there are other targets too
What can attackers who have infiltrated the BIOS do?
  Anything the hardware lets them!
  If the processor can reach out and touch it, then infiltrating the BIOS gives you power over it

## Slide 12: Introducing vulnBIOS
Here is the system we will be using to demonstrate all our vulnerabilities
It is a Dell Latitude E6400 running a customized BIOS (customized by us)
  We made it as vulnerable as can be, which is not how it came from the vendor
  It serves as a good learning tool, I think
  The vendor has already deprecated this codebase and moved on to UEFI
  We cannot state enough that the content in this course, although demonstrated on a laptop running a legacy BIOS is just as applicable to systems running UEFI BIOS

## Slide 13: If you want to follow along…
Optionally, you may want to follow along on your own machine. There are tools which appear to provide the same capabilities as RW-Everything
Mac OS X: Darwin Dumper
  Info: http://www.insanelymac.com/forum/topic/282794-darwindumper/
  Download: https://bitbucket.org/blackosx/darwindumper/downloads
UEFITool
  Src: https://github.com/LongSoft/UEFITool
  Binary: http://www.sendspace.com/folder/ffit0j (URL from the "issues" -> "no docs" page by the author in the source repository)
Linux: lspci, fmem, ChipSec, and Flashrom
  FMEM: http://hysteria.sk/~niekt0/fmem/
  Example of FMEM use in Tools description, since that one may be new to you
  lspci PCI utilities has been around a long time
  http://flashrom.org/Downloads
  https://github.com/chipsec/chipsec
    Mind the https://github.com/chipsec/chipsec/blob/master/source/tool/WARNING.txt ;)

## Slide 14: Running Copernicus
Can be downloaded from:
http://www.mitre.org/capabilities/cybersecurity/overview/cybersecurity-blog/copernicus-question-your-assumptions-about
Locate the Copernicus folder and change to that directory in a CMD prompt
Execute the standalone.bat

## Slide 15: Running Copernicus
Copernicus drops it’s output into the base of the C:\ drive
We’ll talk about a few of these files
The size of this binary will equal the size of your SPI flash
Copernicus dumps all the flash contents (whether readable or not)
For regions which the CPU/BIOS has no permission to read, it writes all 1’s (0xFF)
*Note: badbios.hdr is just the joke-name of the vulnerable BIOS image I created for this class. I changed it!

## Slide 16: Copernicus_BIOS.bin
This is a dump of the entire flash BIOS
Flash is accessed via the programming registers
Copernicus currently ignores flash master permissions and dumps the binary anyway
  Reason: to preserve the flash linear address offsets for each region within the binary

## Slide 17: Copernicus_CSV_Out.csv
This is a comma-separated file containing the configuration data that was read from the system
Not all are security-related
  what ICH/PCH is present
  FREG registers (just to determine the size of each region and the chip)
  Many others
  Because you are attending this class you can access the full .CSV file measurements
  otherwise you are limited only to the most simple SMM/BIOS lock/unlock measurements (but still the most pertinent!)

## Slide 18: Copernicus_Log.txt
Contains a log file of human-readable information about the system which was just measured
Also exit status to determine which, if any, measurements failed

## Slide 19: Running Protections.py
Let’s look at the .CSV file in Notepad++
By the end of the course you’ll know what these mean
Open a CMD prompt in directory C:\Tools\CoP\
> python protections.py per-file C:\
  Can also run per-version, affects the sorting of output
This analyzes our .CSV file for the most basic configuration settings
SMRAM unlocked in the image above is a bug that should be fixed in the version you're using
Anyway, let’s get started on the course!
Notes: TODO talk to scornwell about this

## Slide 20: Some Useful Tools of the Trade

## Slide 21: Copernicus
Question your assumptions
Copernicus is a tool we wrote to determine how prevalent vulnerable BIOS’ are “in the wild”
Collects the information we are discussing during this class
  BIOS_CNTL, SPI, Chipset settings, etc.
  Data can be analyzed offline to determine the vulnerability of BIOS’ in an organization
So far it has been run on nearly 10,000 systems
Runs as a Windows driver (32-bit and 64-bit supported)
  It had to be written fast and cheap; therefore “good” got left out
  Linux and BSD implementations are on their way
Will eventually be released to open source when we have collected enough data to support a whitepaper on our findings
  Source code released in a code for data agreement
  Data run on many, many systems

## Slide 22: RW Everything (RW-E)
http://rweverything.com/
Powerful utility to observe and/or modify platform hardware configurations
Scriptable so you can test ideas without writing a driver
Access to PCI Config space, IO space, physical memory
Freeware, not open source

## Slide 23: Darwin Dumper
https://bitbucket.org/blackosx/darwindumper/downloads
If it doesn’t work, you may be able to get the BSD port of PCI Utilities (LSPCI) to view the PCI Configuration space
Mac Memory Reader may provide the memory dumping capabilities
http://cybermarshal.com/index.php/cyber-marshal-utilities/mac-memory-reader
I don’t know if OS X restricts access to regions in /dev/mem

## Slide 24: FMEM (Linux)
FMEM is a little known Linux kernel module that provides you access to all physical memory in a system
FMEM creates /dev/fmem
Very useful, since /dev/mem restricts access to various regions
  http://hysteria.sk/~niekt0/fmem/
Examples of its use:
Dumps the last 2 MB of system RAM (FFE00000h – FFFFFFFFh)
dd = /dev/fmem of=~/foo.bin bs=1048576 skip=4094 count=2
Therefore, to dump the last 4 MB of memory:
dd = /dev/fmem of=~/bar.bin bs=1048576 skip=4092 count=4
Block size (bs) is 1 MB decimal, you can play with bs, skip, and count to make it less obfuscated (or script it)
So we’re skipping <skip> blocks, then reading <count> blocks

## Slide 25: HxD (hex editor for Windows)
http://mh-nexus.de/en/hxd/
Good & solid hex editor for Windows
Lots of features, including file diffing, raw HD access, etc
  Only thing we want more is speculative x86 disassembly

## Slide 26: IDA Pro
https://www.hex-rays.com/products/ida/
Free version (5.0) works for this class (minus pseudo-code of course)
  https://www.hex-rays.com/products/ida/support/download_freeware.shtml
OllyDbg is good to, probably better than IDA Free

## Slide 27: Snare’s ida-efi Utilities
https://github.com/snarez/ida-efiutils
Behemoth.h
  UEFI structures to import into IDA Pro, makes code readable
EfiGuids.py
  Big honking list of EFI Guids parsed from various sources
And others, but the above two I use most often

## Slide 28: EFIPWN (by G33KatWork)
https://github.com/G33KatWork/EFIPWN
EFI image parser, pulls out .efi modules/drivers
Written in Python, works on everything. Great utility.
Prints the PE file structure of an image
Can Dump the PE file contents into a file system structure
Generating an FDF file to regenerate an image using the EDK2 build system (have not yet tested this)

## Slide 29: UEFITool (by NikolajSchlej)
Succeeds in extracting some files that EFIPWN misses (such as DXE drivers on HP Elitebook 2540p dump)
HP's too cool for a trampoline, they use trebuchets!
https://github.com/LongSoft/UEFITool
Notes: https://medievalreader.files.wordpress.com/2011/08/trebuchet_copy.jpg

## Slide 30: UEFI Firmware Parser (by Ted Reed)
https://github.com/theopolis/uefi-firmware-parser
Can now also extract some stuff that EFIPWN misses
Automatically identifies the possible usage of a file based on the file GUID
  But it can misidentify things which may use the same GUIDs across different vendors (but misidentification is not that big of a deal, since it still gives you a potentially useful name)

## Slide 31: Chipsec
Intel’s open source firmware measurement tool
Yuriy Bulygin and John Loucaidis (Intel) introduced this tool at CanSecWest 2014
https://github.com/chipsec/chipsec
Developers can add new measurement modules to it
Can be run from Windows, Linux, or UEFI Shell

## Slide 32: OpenTPM
https://code.google.com/p/opentpm/
Open Source utility written by Corey Kallenberg
Allows you to retrieve quotes of your TPM PCRs (will be covered in Trusted Computing portion of the class)
Linux users can use the tpm_bios and tpm modules to do this

## Slide 33: (Basic) Chipset Architecture

## Slide 34: Mobile 4-Series Chipset Block Diagram
This is a hardware model the Mobile 4-Series chipset and its logical relation to the CPU
Specialized chips integrated onto the motherboard that interface the processor to system components.
Two components make up the chipset: the Memory Controller Hub (MCH) and the I/O Controller Hub (ICH)
These components must be configured to be able to sustain an Operating System.
BIOS performs this configuration during boot
I prefer the diagram from the Desktop 4-Series Chipset, which explicitly labels the MCH
Intel Mobile 4-Series Chipset Datasheet, pg. 13
Notes: A fair number of these pertain to security and that’s what we’ll focus on.

## Slide 35: Alternative Block Diagram
For reference, this is the diagram layout I personally (strongly) prefer
But it explicitly labels the MCH
Also lists the SPI device, unlike it’s Mobile counterpart
However, the MCH on the 4-Series chipset connects to an ICH rev.10 rather than an ICH rev. 9, which is not what's present on this example E6400 system
Intel 4-Series Chipset Datasheet, pg. 25
Notes: They are probably similar enough to reference this one instead, but I will not do that.

## Slide 36: Mobile 4-Series Chipset Block Diagram
Memory Controller Hub (MCH)
Interfaces the processor with the rest of the system
Connected via a fast bridge/bus (originally FSB, became HyperTransport (AMD) and QuickPath (Intel), the latter which became DMI (or DMI 2.0)
  From a logical perspective it’s invisible to us for our purposes
Sometimes called the Northbridge
Contains a Memory Controller and an interface for PCI Express graphics
A ‘G’ in front of MCH indicates it has on-board graphics
Intel Mobile 4-Series Chipset Datasheet

## Slide 37: A brief (and final) word about the evolution of busses to the processor
Pictures from https://www-ssl.intel.com/content/dam/doc/white-paper/quick-path-interconnect-introduction-paper.pdf

## Slide 38: (Magic School) Busses cont.
QPI's lowest level protocols are designed for higher reliability and graceful failover in highly multi-processor systems like servers
, 2009
Note that it could also communicate with chipset via QPI
Notes: http://www.scholastic.com/qubo/images/msb-bus.png
http://en.wikipedia.org/wiki/Direct_Media_Interface

## Slide 39: So QPI was used to talk to the chipset, but then was superceded by DMI 2 in SandyBridge

## Slide 40: Memory Controller Hub (MCH)
For this course on BIOS/UEFI security, the aspects of the MCH (or Platform Controller Hub (PCH) as it has evolved to) we care about most are:
  Chipset Configuration registers
  DRAM Controller Registers
In PCH systems the DRAM Controller Registers move into the CPU (we will talk about this in a bit)
Intel Mobile 4-Series Chipset Datasheet, pg. 13
Notes: There are still a lot of systems out there that pre-date the consolidation into the CPU.

## Slide 41
I/O Controller Hub
Interfaces the MCH (and thus the processor) to system devices
Intel Mobile 4-Series Chipset Datasheet

## Slide 42: Low-Pin Count (LPC)
The devices on the ICH which we care about most are:
LPC (Low-Pin Count) controller device
SPI Flash (and somewhat the Firmware Hub)
Trusted Platform Module (TPM)
Notes: These hold true whether the system is an older MCH/ICH system or a new consolidated PCH system

## Slide 43: Trusted Platform Module (TPM)
Extends the security functions within the TPM chip to the CPU/system
Memory-Mapped (fixed address)
Software operation is still the same when the ICH is consolidated into a PCH
Intel I/O Controller Hub 9 Datasheet, because it includes a more complete block diagram
Notes: These hold true whether the system is an older MCH/ICH system or a new consolidated PCH system

## Slide 44: Serial-Peripheral Interface (SPI)
It’s where the BIOS binary resides
CPU execution starts here upon system startup
Interface to the device is Memory-Mapped
We’ll cover memory-mapping in the Address Space portion of the course
From a software development, configuration is still the same when the ICH is consolidated into a PCH
(This is the Firmware Hub (FWH). We’ll cover this when
we talk about SPI.)
Intel I/O Controller Hub 9 Datasheet, because it includes a more complete block diagram
Notes: These hold true whether the system is an older MCH/ICH system or a new consolidated PCH system

## Slide 45: Evolution to Platform Controller Hub (PCH)
Intel 4-Series Chipset Datasheet
Bottleneck reduction
Memory Controller moved into the CPU
  AMD did this in ~2003 with Athlon64
  Intel ~2008 (Core i-series CPU)
Graphics processing unit too
The Northbridge was essentially eliminated to form a single component (PCH)
Overall trend is to move high-bottleneck areas closer to the CPU which has the fastest clock on the system

## Slide 46: Now everything’s just PCHy
Shown here is the Intel 5-series chipset
First iteration of the consolidation into a single Platform Controller Hub (PCH)
AMD did similar in 2003, but I don’t want to throw too many hardware diagrams at you (despite being different at the hardware level, logically they are similar if not the same)
Better to show you just a few, explain why they are the way they are so then you can interpret new/different ones yourself
Processor is starting to resemble a System On a Chip (SoC)
Intel Core i5-600, i3-500 Desktop Processor Series, Intel Pentium Desktop Processor 6000 Series datasheet
(PCH)
Notes: No more diagrams like the previous, no good block diagram of a PCH
The Chipset no longer consists of 2 components but of a single component, PCH

## Slide 47: Platform Controller Hub (PCH)
All the ICH components that we cared about for this course are still present
  From a software standpoint, even their mode of access is the same
Functionally speaking, most of what we’ll be looking at is agnostic as to whether its MCH/ICH or PCH
  There are a few exceptions and those will be addressed as they crop up as well as how you account for them
Intel Core i5-600, i3-500 Desktop Processor Series, Intel Pentium Desktop Processor 6000 Series datasheet
(PCH)
Notes: No more diagrams like the previous, no good block diagram of a PCH
The Chipset no longer consists of 2 components but of a single component, PCH

## Slide 48: Software Model
This is how the processor sees the chipset devices
Not actually a complete diagram, there are more devices listed in the datasheet than what Intel included in this diagram
Some devices have additional functions (it’s a PCI-thing which we’ll talk about)
* Device 2 won’t be implemented if there is an external graphics card.
Notes: How your CPU sees the hardware

## Slide 49: Device 0: DRAM Controller
Device 0 – DRAM Controller
Configured by BIOS to define much of the memory map
  SMM
  PCI Express base address register space(PCIEXBAR)
  Etc.
Notes: How your CPU sees the hardware

## Slide 50: Device 31: LPC Interface Bridge
Device 31 – Low Pin Count Interface (LPC) Bridge
Located on ICH (or PCH if it’s a PCH system)
Implements various system management functions
We reference this device a lot
Spec: http://www.intel.com/design/chipsets/industry/25128901.pdf (Low Pin Count Interface Specification, Revision 1.1)
Notes: How your CPU sees the hardware

## Slide 51: Datasheet will list all PCI Devices
So as I said, there are devices which were not included in the chipset diagram provided by Intel in the Mobile 4-Series datasheet.
They’re not all important from a security perspective, but provided here for reference
*Intel I/O Controller Hub 9 datasheet

## Slide 52: Chipset Identification
Goal: Identify the Chipset and/or Controller Hub
Reasons: (1) To find the datasheet, and (2) know the locations of those registers which we will be probing to determine whether a system is vulnerable
  Some have stayed the same (same name, same offset) over the years (LPC, BIOS_CNTL) while others have “bounced around a little”
  Our demonstrations/slides are all on the Mobile 4-Series Chipset and IO Controller Hub Family 9
  However, the functionality provided by these registers still exist in the latest architecture (assuming they aren’t just still the “same old registers”)
  I want you to be able to locate/analyze these for evaluation (ie: teaching you to fish)
Ok I’m convinced! So how do we find out?
  We are “pretending” that we don’t have eyes on the platform itself:
  In other words, we are using RW-Everything in this example, but RW-E accesses the PCI configuration space which we also could do programmatically
Notes: Sort of like a lab

## Slide 53: Strategy:
Many of the registers we care about are located in two separate devices: (1) LPC Device, and (2) DRAM-Controller
In legacy Chipsets the LPC device is located in the IO Controller Hub and the DRAM-Controller is located in the Memory Controller Hub
The datasheet containing the information related to the DRAM controller will be found in the Chipset datasheet
The datasheet containing the LPC-related information will be found in the “I/O Controller Hub” datasheet
DRAM Controller
LPC Device
Chipset
Datasheet
ICH
Datasheet
Notes: Sort of like a lab

## Slide 54: Strategy:
Many of the registers we care about are located in two separate devices: (1) LPC Device, and (2) DRAM-Controller
In Modern "Chipsets" (PCH) the LPC device is located in the Platform Controller Hub and the DRAM-Controller is located in the Processor
The datasheet containing the information related to the DRAM controller will be found in the processor datasheet
The datasheet containing the LPC-related information will be found in the Chipset datasheet
DRAM Controller
LPC Device
CPU
Datasheet
"Chipset"
Datasheet
Notes: Sort of like a lab

## Slide 55: Strategy: Additional Notes
You do not have to know in advance whether the architecture is a modern chipset or otherwise, the process of identifying the device ID’s will tell you that
Because we’re identifying PCI devices, this same strategy will work on an AMD system (which is completely left out in this course)
  However, identifying the applicable registers and offsets is an exercise left to you (or me if I get my hands on an enterprise system with an AMD processor)
Notes: Sort of like a lab

## Slide 56: Get the LPC Device ID
Will tell us the Controller Hub family (therefore either ICH datasheet if legacy or chipset datasheet otherwise)
Bus 0, Device 31 (1Fh), Function 0, Offset 2 (2-bytes)
Not sure where RW Everything gets the names of its PCI devices from
In this example, the LPC Device ID is 0x2917
Notes: Sort of like a lab

## Slide 57: Device ID Lookup
http://pciids.sourceforge.net
http://pci-ids.ucw.cz/ (same site, alternate location)
Device ID 0x2917 is part of the ICH9M-E family
http://www.intel.com/content/www/us/en/io/io-controller-hub-9-datasheet.html
Notes: Sort of like a lab

## Slide 58: Get the Memory Controller Device ID
Read the 2-byte Device ID of the Memory Controller:
Bus 0, Device 0, Function 0, Offset 2
In this case RW Everything calls it a Host bridge, but as you can see at offset 0x0E in it’s header, it is not a bridge
  PCI-related fact which we’ll cover in PCI
In this sample case the Memory Controller Device ID is 0x2A40
Notes: Sort of like a lab

## Slide 59: Device ID Lookup
http://pciids.sourceforge.net
http://pci-ids.ucw.cz/ (same site, alternate location)
Device ID 0x2a40 is part of the Mobile 4-Series chipset family
http://www.intel.com/assets/PDF/datasheet/320122.pdf
Notes: Sort of like a lab

## Slide 60: So what we have learned about this E6400
The LPC Device ID is 2917h
  ICH9M-E Controller Hub
  Member of the IO Controller Hub 9 family
The Memory Controller Device ID is 2A40h
  Mobile 4-Series Chipset Memory Controller
Therefore this is a legacy chipset
  DRAM controller is located in the chipset
  LPC is located in the IO Controller Hub
The same steps will work on a new system
  The DRAM controller will be located on the processor
  The LPC device will be located in the chipset (aka: platform controller hub)
Sometimes there may be ambiguity, let’s take a look at one where this happens, and it just happens to be a PCH system. Let’s figure out how to tell

## Slide 61: Solving Ambiguity: Get LPC Device
As before, Read the 2-byte Device ID of the LPC device:
Bus 0, Device 31d (1Fh), Function 0, Offset 2
If the Controller Hub is referred to as the Chipset, it’s a PCH device.
So in a PCH system, the LPC controller will tell us the chipset family
So this is a QM67 Express Chipset (6-series chipset)
Datasheet: http://www.intel.com/content/www/us/en/chipsets/6-chipset-c200-chipset-datasheet.html
Notes: Sort of like a lab

## Slide 62: Identify the MCH Device ID
As before, Read the 2-byte Device ID of the MCH (DRAM Controller):
Bus 0, Device 0, Function 0, Offset 2
In this sample case the Memory Controller Device ID is 0x0104
2nd Generation Core processor Family
However there are separate datasheets for the 2nd generation Mobile and Desktop family datasheets
To identify the CPU, we have to download the Specification updates for each
Notes: Sort of like a lab

## Slide 63: Hmm…Either Mobile or Desktop* CPU
Download the Specification Updates for both the Desktop and Mobile family (2nd generation Core series processor)
  http://www.intel.com/content/dam/www/public/us/en/documents/specification-updates/2nd-gen-core-family-mobile-specification-update.pdf
  http://www.intel.com/content/dam/www/public/us/en/documents/specification-updates/2nd-gen-core-desktop-specification-update.pdf
In this case, the DRAM Controller (MCH) device ID of 0104h is defined in the Mobile series specification update
*We’re operating under the assumption that this is being done remotely so we can’t just “look.”
Notes: Sort of like a lab

## Slide 64: Get the CPU Stepping Information
When EAX initialized with a value of ‘1’, CPUID returns the Extended Family, Extended Model, Processor Type, Family Code, Model Number and Stepping ID value (in EAX)
You can run CPUID in RW Everything
  CPUID requires no privileges to run
Notes: Sort of like a lab

## Slide 65: Identify the CPU Stepping Information
Extended family tells you which processor family the CPU is of (Pentium, Pentium Pro, Intel Core, etc.)
Extended Model identifies the particular model within the family
Processor Type tells you if it’s OEM, etc.
Family Code corresponds to EDX bits [11:8] at system reset
The Model Number corresponds to EDX bits [7:4] at system reset
    This is a PCH example and so this CPUID return will differ from our EDX value from the entry vector portion of the course which was of the E6400
  Stepping ID is the revision number of this CPU model
Gen2 Core Specification Update Datasheet
Notes: Sort of like a lab

## Slide 66: Beware: Gotcha #1
Verify the Device ID you look up is for the correct vendor
  Different Vendors can use the same Device IDs
  Vendor ID’s are allocated by the PCI SIG and are always unique
The above Memory Controller Device ID of 0104h returns multiple hits on http://pci-ids.ucw.cz
  But it’s the 8086h (Intel) one that we want

## Slide 67: Beware: Gotcha #2
It’s good to cross-reference more than one source...
Where one fails (either returns an incorrect device, or finds no device at all), another may succeed
www.PCIDatabase.com

## Slide 68: Further Observations:
The above method will work for any PCI device located on the PCI Bus
There probably won’t be datasheets (publically) available for every PCI device on your system
It’s up the vendor as to the amount of information they wish to make public
TPM datasheets are a good example
Be wary of the gotcha’s
  http://pciids.sourceforge.net is also used by the LSPCI utility for Linux
  has always been reliable for me
  their human-readable device names are intuitive

## Slide 69: Specification Updates
For an Intel system, a given device family (Processor, IO Controller Hub, Chipset) will have a separate datasheet entitled “Specification Update”
The spec update provides typo-fixes and such but also provides the device ID’s for each revision within that particular device family
ICH Family 9 Specification Update

## Slide 70: BIOS Boot Process Summary
A “simple” process…

## Slide 71
This covers an example of a minimal BIOS boot process, just to give an idea of what the BIOS does before your operating system starts to load.
It doesn’t include everything of course because it’s geared towards minimal-configuration to achieve 100% functionality.

## Slide 72: Boot Process at a glance*
*This list composed from Intel Minimal Architecture Boot Loader
Power-up
  16-bit Real Mode accessing address FFFF_FFF0h
Operating Mode Selection
  Flat Protected Mode
Preparation for Memory Initialization
  CPU Microcode Update
  Set up CPU Cache as RAM (CAR)
  Chipset Initialization (MCHBAR, PCIEXBAR, etc.)
Memory Initialization
  Configure the Memory Controller
Post Memory Initialization
  Memory test
  Copy firmware from flash to memory for faster execution*
    In the doc this is listed as firmware shadowing but I’m modifying it somewhat since the BIOS can perform the copying of flash components to memory
    As a general rule, it’s better to copy things to memory before execution as soon as possible
  Memory Transaction Re-Direction (PAM registers)
  Setting up the Stack (before memory initialization, stack will be in CPU cache)
  Transfer to DRAM (the BIOS flash that was copied to memory is now executed)
Notes: Acronyms not yet defined:
PAM = Programmable Attribute Map

## Slide 73: Boot Process at a glance*
*This list composed from Intel Minimal Architecture Boot Loader
Miscellaneous Platform Enabling
  Platform dependent: Initialize clocks to operate at N Hz, configure general-purpose I/O, etc.
Interrupt Enabling - PIC (Programmable Interrupt Controller), LAPIC (Local Advanced PIC), I/O APIC, etc.
Interrupt Tables
  Interrupt Vector Table (IVT)
    Interrupt Service Routine (ISR) – INT 10h, etc…
  Interrupt Descriptor Table (IDT)
    Exceptions
Setting up timers
  In ICH: RTC (, HPET, 8254 Programmable Interrupt Timer (PIT), TCO timer (used as watchdog)
  In CPU: LAPIC timer
Memory Caching Control
Processor Discovery and Initialization
  CPUID
  Startup Inter-Processor Interrupts (SIPIs) are written to a processor’s LAPIC telling it to wake up and where to start executing code at (must be a 4KB aligned boundary)
    Intel SW Programmer’s Guide has more detail on this
  Each processor will awaken in Real Mode
Notes: Acronyms not yet defined:
RTC = Real Time Cock
HPET = High Performance Event Timer
TCO = "In this document the acronym TCO (Total Cost of Ownership) refer to a logic block in the Intel ICH products family. The Watchdog Timer (WDT) is one of the functions of that logic block."

## Slide 74: Boot Process at a glance*
*This list composed from Intel Minimal Architecture Boot Loader
I/O Devices
  Super I/O can control PS/2 keyboard, serial, parallel, etc. interfaces
PCI Device Discovery
  Enumerate PCI devices
  Assign address space (port IO, Memory Mapped IO)
  Detect and execute Expansion ROMs (XROMs)
Memory Map
  Region Types
    Memory
    Reserved
    ACPI Reclaim
    ACPI NVS
    ROM
    IOAPIC
    LAPIC
  Region Locations
    Consult your datasheet for a complete list, but we’ll cover some of the more relevant ones
Non-Volatile (NV) Storage
  CMOS
  NV Flash
Handoff to boot-loader

## Slide 75: Only 16 steps? BIOS is simple!
*This list composed from Intel Minimal Architecture Boot Loader
Easy to summarize, not so easy to implement
Very complex implementations
Even if it’s only a couple MB, it’s a very DENSE couple of MB
That list taken from the Intel Minimal Architecture Boot Loader which provides a pretty good list of functional requirements
What is left out is:
  Initializing SMM and locking down SMRAM
  Locking down the BIOS Flash

## Slide 76: Entry Vector Execution Environment
In the beginning…

## Slide 77: Processor State After Reset
EAX, EBX, ECX, EBP, ESI, EDI, ESP are all reset to 0
EDX contains the CPU stepping identification information
  Same info returned in EAX when CPUID is called with EAX initialized to ‘1’
  *This will vary of course, the value in the table to the left corresponds to the Core2Duo inside the E6400
The base registers are 0 with the exception of CS which is initialized with F000
EIP (or IP since it’s 16-bit mode) is initialized with (0000)FFF0
  CS:IP = F:FFF0h
EFLAGS is 00000002h
  Only hard-coded bit 1 is asserted
  If I were sitting at a breakpoint at the entry vector, then bit 16 (resume flag) would be asserted indicating that debug exceptions (#DB) are disabled.
Name | Value
EAX | 00000000
EBX | 00000000
ECX | 00000000
EDX | 00010676*
EBP | 00000000
ESI | 00000000
EDI | 00000000
ESP | 00000000
CS | F000
DS | 0000
SS | 0000
ES | 0000
FS | 0000
GS | 0000
EIP | 0000FFF0
EFLAGS | 00000002
E6400 Registers at Reset

## Slide 78: Processor State After Reset: Control Registers (CRs) (add more info)
Control registers CR2, CR3, and CR4 are all 0
CR0 is 6000_0010h (likely since Pentium)
Paging (bit 31) is disabled
  All linear addresses are treated as physical addresses
Cache Disabled (bit 30) is set
Not-Write-through (bit 29) is set
Bits 30 and 29 refer to caching and ensure that CPU caching is disabled and that Write-Back caching in particular is disabled
  We’ll talk about that in the System Management Mode (SMM) section since there was a high profile attack on SMM using caching
Most notable bits are high-lighted

## Slide 79: Processor State After Reset: Control Registers (CRs) (add more info)
Alignment Mask (bit 18) is 0
Write Protect (bit 16) is 0
Numeric Error (bit 5) is 0
Extension Type (bit 4) is set (hard-coded math coprocessor support)
Task Switched (bit 3) is 0
Emulation (bit 2) is 0
Monitor Coprocessor (bit 1) is 0
Protection Enable (bit 0) is 0
  0 indicates that we are in Real Mode
  1 indicates we are in Protected Mode
Most notable bits are high-lighted
Notes: http://www.quickmeme.com/img/09/09853f2d5498f2b24d0147b5ea71ef1e8b383494a1e9b2e722ac461e737ea7ca.jpg

## Slide 80: Entry Vector (aka: Reset Vector)
System Memory
BIOS Flash Chip
0
4GB
www.intel.com/.../datasheet/io-controller-hub-9-datasheet.pdf
0xFFFFFFF0
LPC I/F
At system reset, the active processor begins execution at the reset vector
The reset vector is always located on flash at "memory" address FFFF_FFF0h
  The whole chip is mapped to memory but not all of it is readable due to protections on the flash device itself

## Slide 81: Reset Vector Decoding
System Memory
BIOS Flash Chip
0
4GB
www.intel.com/.../datasheet/io-controller-hub-9-datasheet.pdf
0xFFFFFFF0
LPC I/F
Decoding (routing) is performed via decoders located in the chipset
As far as the CPU is concerned it is fetching instructions from memory
But in fact it’s from Flash BIOS

## Slide 82: Mini-Lab: BIOS Flash Decoding
Let’s look at some of the decoding (routing) of the BIOS to memory
Open RW Everything and click on the PCI tab to open up the PCI window
Click the drop-down tab and select Bus 00, Device 1F, Function 00
This is the LPC device
Click on the Word 16 bit button to arrange the PCI configuration registers into 16-bit words
Notice word offset D8-D9h

## Slide 83: Mini-Lab: BIOS Flash Decoding
Offset D8-D9h is FWH_DEC_EN1
As stated, this controls the decoding of ranges to the FWH
If your system uses SPI and not a Firmware Hub (and it does since FWH is very rare), it still decodes to the SPI BIOS
We want bit 14 which decodes FFF0_0000h – FFF7_FFFFh
The BIOS flash on the E6400 is 1A_0000h bytes long (we’ll cover how to determine this in the flash BIOS section of class)
4GB – 1A_0000h = FFE6_0000h
Therefore, this bit is responsible for decoding a lower range of the BIOS

## Slide 84: Mini-Lab: BIOS Flash Decoding
Therefore, with FWH_DEC_EN bit 14 asserted, we’re decoding to a portion of BIOS binary
Click Memory button and type address FFF00000

## Slide 85: Mini-Lab: BIOS Flash Decoding
De-assert bit 14 (set to 0xBFCC)
Decoded to memory now
This memory range is still read-only
This example is to help provide a picture of the initial boot environment

## Slide 86: Mini-Lab: BIOS Flash Decoding
Reset it back to 0xFFCC
Couple of notes:
Your original values may differ since BIOS flips them on and off as the developers decided necessary
You can also take the “lazy” route to clear it and set it to 0x0000
Likewise you can set it to 0xFFFF to assert all the FWH decoders
Bit 15 is Read Only and always asserted

## Slide 87: Pop Quiz!
Why do you suppose bit 15 is RO and always asserted?

## Slide 88: Mini-data-collection Lab: Entry Vector in BIOS Binary
If we dump the BIOS and look at it in a hex editor, at the end of the file we will see a jump instruction (near, relative jump)
The chipset aligns the flash so that the limit of the BIOS region (always either the only/last region on the flash) aligns with address FFFF_FFF0h
The CPU executes these instructions in 16-bit Real Mode
Notes: This could be a lab. Have students dump and everyone says what they have at their entry vector (because sometimes it has nops, sometimes it doesn't, etc)

## Slide 89: Real-Address Mode (Real Mode)
The original x86 operating mode
Referred to as “Real Mode” for short
Introduced way back in 8086/8088 processors
Was the only operating mode until Protected Mode (with its "virtual addresses") was introduced in the Intel 286
Exists today solely for compatibility so that code written for 8086 will still run on a modern processor
  Someday processors will boot into protected mode instead
In the BIOS’ I have looked at, the general theme seems to be to get out of Real Mode as fast as possible
Therefore we won’t stay here long either

## Slide 90: Real Mode
16-bit operating mode
Segmented memory model
When operating in real-address mode, the default addressing and operand size is 16 bits
An address-size override can be used in real-address mode to enable access to 32-bit addressing (like the extended general-purpose registers EAX, EDX, etc.)
However, the maximum allowable 32-bit linear address is still 000F_FFFFH (220 -1)
So how can it address FFFF_FFF0h?
  We’ll answer that in a bit

## Slide 91: Real Mode Addressing: Segment Registers
CS, DS, SS, ES, FS, GS
Only six segments can be active at any one time
16-bit segment selector contains a pointer to a memory segment of 64 Kbytes (max)
16-bit Effective address can access up to 64KB of memory address space
Segment Selector combines with effective address to provide a 20-bit linear address
So an application running in real mode can access an address space of up to 384 KB at a time (including stack segment) without switching segments

## Slide 92: Real Mode Addressing
Intel Developers Manual, 20.1.1
As shown in Figure 20-1 in the Intel SW Developers guide
The Segment Selector (CS, DS, SS, etc.) is left-shifted 4 bits
The 16-bit Segment Selector is then added to a 16-bit effective address (or offset if you will) within the segment
Remember, upon entry into the BIOS, all linear addresses are translated as physical (per CR0)

## Slide 93: Real Mode Addressing Problem: Overlap
Intel Developers Manual, 20.1.1
Addresses in different segments can overlap
Given such a limited environment it’s no wonder we want to choose a different operating mode as soon as possible

## Slide 94: F:FFF0 != FFFF:FFF0
Every segment register has a “visible” part and a “hidden” part.
Intel sometimes refers to the “hidden part” as the “descriptor cache”
It’s called “cache” because it stores the descriptor info so that the processor doesn’t have to resolve it each time a memory address is accessed
Notes: The information cached in the segment register (visible and hidden) allows the processor to translate addresses without taking extra bus cycles to read the base address and limit from the segment descriptor.

## Slide 95: Descriptor Cache
“When a segment selector is loaded into the visible part of a segment register, the processor also loads the hidden part of the segment register with the base address, segment limit, and [access information] from the segment descriptor pointed to by the segment selector.”
Real Mode doesn’t have protected mode style access-control so the [access information] part is ignored
This means that the hidden part isn’t modified until after a value is loaded into the segment selector
So the moment CS is modified, the CS.BASE of FFFF_0000H is replaced with the new value of CS (left shifted 4 bits)
Intel SW Dev, Vol 3, Sec 3.4.3

## Slide 96: CS.BASE + EIP
CS.BASE is pre-set to FFFF_0000H upon CPU reset/power-up
EIP set to 0000_FFF0H
So even though CS is set to F000H, CS.BASE+EIP makes FFFF_FFF0H
So when you see references to CS:IP upon power-up being equal to F:FFF0h, respectively, now you know how what it really means and how it equates to an entry vector at FFFF_FFF0h
Vol. 3, Figure 9-3

## Slide 97: Entry Vector
So upon startup, while the processor stays in Real Mode, it can access only the memory range FFFF_0000h to FFFF_FFFFh.
If BIOS were to modify CS while still in Real Mode, the processor would only be able to address 0_0000h to F_FFFFh.
  PAM0 helps out by mapping this range to high memory (another decoder)
So therefore if your BIOS is large enough that it is mapped below FFFF_0000H and you want to access that part of it, you best get yourself into Protected Mode ASAP.
  And this is typically what they do
Notes: What you talkin ‘bout Willis?

## Slide 98: Analyzing a BIOS Binary
We’re going to take a quick look at how to get past the entry vector to where the real chipset initialization begins
From the point of view where you assume to know nothing about how this BIOS handles the entry vector
Afterwards I’ll provide an “ugly shortcut” method that gets you to the same place, but faster
From there it will just be Legacy BIOS analysis “as usual”
  Proprietary structures, etc.
Contrasted with UEFI whose structures, etc. are publically available
Notes: What you talkin ‘bout Willis?

## Slide 99: 1: Disassemble the BIOS Binary
Acquire a dump of the BIOS flash from a tool like Flashrom or Copernicus and open it in IDA
Intel 80x86 metapc setting is fine regardless of IDA version
Choose to disassemble in 32-bit mode
Not a typo, most BIOS’ jump into 32-bit protected mode as soon as possible
  If your BIOS is much older, just edit the segment to 16-bit
I have the full version of IDA Pro but am using Free version 5.0 to show you that this works with that version
Other debuggers like OllyDbg should also work
Notes: What you talkin ‘bout Willis?

## Slide 100: 2: Rebase the Program
First thing we’re going to do is rebase the program
We know the entire image of this BIOS is mapped to memory so that its upper address boundary is at FFFF_FFFFh with the entry vector at FFFF_FFF0h
Let’s touch these up to reflect this
Notes: What you talkin ‘bout Willis?

## Slide 101: 2.1: Rebase the Program
In this lab our file contains only the BIOS portion of the flash.
The value to enter is:
4 GB – (Size of BIOS Binary)
For this lab it is 0xFFE60000
  (for BIOS Length 1A0000h)
Example: If you had a 2 MB BIOS binary you would rebase the program to FFE0_0000h
The idea is for the entry vector at FFFF_FFF0h in memory to be displayed in IDA at linear address FFFF_FFF0h
If you encounter a size-related error, open the binary file with a hex editor (like HxD) and delete the last byte. Then re-open the binary in IDA and rebase it. Still treat it like it were its original size.
!
Notes: What you talkin ‘bout Willis?

## Slide 102: 2.2: Rebase the Program
You know you have done it right when you see executable instructions at FFFF_FFF0h, such as:
E9 3D FE
E9 is a relative JMP instruction (JMP FE3Dh)
Note: The JMP instruction may be preceded by a WBINVD instruction or a couple NOP instructions
  In this case, these instructions will be at FFFF_FFF0h instead of the JMP
There always will be a JMP here following those
Notes: What you talkin ‘bout Willis?

## Slide 103: 3. Determine IDA Segments: Manually Analyze the Entry Vector JMP
So now we want to create some IDA segments to help us (and IDA) interpret the disassembly
One goal is to keep the 16-bit segment that contains the entry vector as small as possible
  From experience, BIOS takes a FAR JMP away from here after entering protected mode
JMP FE3Dh is relative to the address following the JMP:
FFFF_FFF3h, in this case
Notes: What you talkin ‘bout Willis?

## Slide 104: 3.1: JMP rel16
The address following our JMP instruction is FFFF_FFF3h
  We’ll treat it like a 64KB segment (FFF3h) for easier readability
  Technically it is a 64KB segment so we don’t have to worry about this assumption throwing off our calculation
Take the 2’s compliment of the operand in the JMP FE3Dh instruction:
  (FE3Dh – 1) = FE3Ch
  ~FE3Ch = 01C3h
Subtract this displacement from the address following the JMP instruction to find the destination:
FFF3h – 01C3h = FE30h
Intel SW Developers Guide, Vol. 2, Intel Instruction Set Reference
Notes: What you talkin ‘bout Willis?

## Slide 105: 3.2: Determine Segment Boundary
So we know the destination of the JMP at the entry vector is FFFF_FE30h
We can now make an assumption that the address FFFF_FE00h can serve as a segment boundary for us
Our goal is to keep the segment containing the entry JMP as small as possible
The assumption is that code will be aligned and will take a far JMP to a lower address space
This assumption is based on experience, but could vary
Remember these are segments to help IDA translate our disassembly, not necessarily mimic the system
Notes: What you talkin ‘bout Willis?

## Slide 106: 4: Create Initial 16-bit Segment
Edit –> Segments –> Create Segment
Pick any segment name you want
Class can be any text name
16-bit segment
Start Address = 0xFFFFFE00
End Address = 0xFFFFFFFE
  Remember: IDA Does not like the address FFFFFFFF (-1) !!
  Actually, according to IDA documentation, the 32-bit version of IDA doesn’t “like” any address at or above FF00_0000h 
Base = 0x0FFFF000
  CS.BASE = FFFF_0000h on boot
VirtualAddress = LinearAddress - (Base << 4)
FFF0 FFFF:FFF0 – (Base << 4)
Notes: What you talkin ‘bout Willis?

## Slide 107: 5: Identify Memory Model
Once this segment is created, IDA “automagically” recognizes the destination of the entry vector jump
What we see here is the BIOS preparing to enter protected mode
Likely it will be using a flat memory model
Note the ‘8’ in the far jump operand
That references the entry at offset 8 in the GDT
Now let’s look at that LGDT instruction
Notes: What you talkin ‘bout Willis?

## Slide 108: 5.1: LGDT Instruction
LGDT loads the values in the source operand into the global descriptor table register (GDTR)
The operand specifies a 6-byte structure containing the size of the table (2-bytes) and a 4-byte pointer to the location of the table data
The table data contains segment bases, limits, access rights
More than likely it will be a single base of 0000_0000h and a limit of FFFF_FFFFh
If this is true, then they are using a Flat Memory Model
  And you shall rejoice!
  Really there is no point in not using the flat memory model, you can generally just assume they are
All of the following GDT information is also covered in Intermediate x86
Notes: (remember this from Intermediate x86? ;))
the memory being pointed at contains a 16-bit "selector" (which refers to a segment entry in either the GDT or LDT), and a 32-bit offset from the beginning of the segment the selector refers to. The segment descriptor contains data about the segment, of course...including where in memory it starts

## Slide 109: 5.2: Import GDT/IDT Structures
You can import these structures into IDA by parsing the file “peewee.h”
Screenshot included so you can enter them manually if necessary
IDT structures are also provided
Importing structures like this is very useful for analyzing BIOS
Legacy BIOS is filled with proprietary structure definitions
Contrasted with UEFI structures which are defined in a publically-released standard
http://www.jamesmolloy.co.uk/tutorial_html/4.-The%20GDT%20and%20IDT.html
Notes: What you talkin ‘bout Willis?

## Slide 110: 5.3: Define GdtPtr
Go to the address referenced by the operand to the LGDT instruction
IDA will have already tried to interpret this and failed, undefine that
Now define it as structure of type GdtPtr
As per the structure definition, the first member is the size of the GDT table and the second is a pointer to the location of the GDT entries
That pointer won’t translate properly for us, but we can tell where the entries are defined just by looking at the value
Notes: What you talkin ‘bout Willis?

## Slide 111: 5.4: Define GDT Entries
We know it’s location is in our 16-bit segment
Manually go there by jumping to seg:FF00
This is where the GDT entries are defined
Look at the structure definition in peewee.h to interpret
The table size is 0x78 bytes, but we only want the second entry into the table at offset 8:
BASE = 0000_0000h
LIMIT = FFFF_FFFFh
This is the flat memory model
These descriptors will be used by the subsequent code so you can fill out the rest as needed
*There may be a superior way to set up our segments so that it all “just works”
but I have not found it yet. Also, disregard the different segment names.
Notes: What you talkin ‘bout Willis?

## Slide 112: 5.5: Full GDT
The GdtEntry structure definition in peewee.h can be used to interpret the GDT entries
Each structure is 8 bytes in size
The FAR JMP is referencing the second entry (offset 8)
Base 0, Limit FFFF_FFFFh
Notes: What you talkin ‘bout Willis?

## Slide 113: 5.5: Full GDT
Here is the entire GDT for reference. You don’t need an expensive debugger to analyze BIOS (but it does save a lot of time)
Notes: What you talkin ‘bout Willis?

## Slide 114: 6: Create the 32-bit BIOS segment
Now create the 32-bit segment
Start address is FFFF_FFFFh - <size of the BIOS region> + 1
  FFFF_FFFFh – 1A_0000h in this example
  SPI regions will be explained more during BIOS flash portion of the course
End Address is our segment boundary Address
  FFFF_FE00h in this example
Base Address matches that of the GDT table, entry 8 (0000_0000h)
Copernicus_Log.txt
Notes: What you talkin ‘bout Willis?

## Slide 115: 7: Touch up the Far Jump
So we know that this is loading the descriptor entry at offset 8 in the GDT
We can visually inspect the operand of this JMP to see that it’s going to FFFF_0100h
We can manually fix this operand
Right click the operand and select ‘Manual’
Change it to:
bios:FFFF0100h
Uncheck ‘Check Operand’
A little ugly
Notes: What you talkin ‘bout Willis?

## Slide 116: Welcome to BIOS Analysis
Converting the binary at FFFF_0100h to code provides you the entry point to the real BIOS initialization
Up until this point everything we covered is pretty standard across many BIOSes
  This applies to UEFI BIOS too
  Even really old BIOS will basically follow the path we took, perhaps staying in real mode longer though
From here on though, if legacy, it’s completely proprietary to the OEM (data structures, etc.)
By contrast, UEFI is standardized from head to toe
Notes: What you talkin ‘bout Willis?

## Slide 117: Why so Ugly? IDA Segments
IDA can’t combine 16-bit and 32-bit instructions in the same segment
We could have created another 32-bit segment to account for the processor entering 32-bit protected mode
But then we’d have to create 4 segments
Not really necessary since we can visually inspect it and determine what’s going on
Fudging it is okay since the important stuff happens after all this
32-bit
16-bit
16-bit
FFFF_FFF0h
FFFF_FE30h
FFFF_FE48h
FFFF_FE51h
32-bit
.
.
.
.
.
.
FFFF_0100h
Notes: What you talkin ‘bout Willis?

## Slide 118: BIOS Entry Vector Analysis: Short Cut 1
You can likely skip a few of the steps and make some assumptions to get to the initialization code faster:
Open your BIOS binary file in IDA same as before
Rebase the program, same as before
Don’t bother analyzing the entry vector JMP, just create a 16-bit segment the exact same as before, except:
  Start Address: 0xFFFFFFF0
  We can count on IDA being smart enough to interpret this properly even though it makes our segment a little odd
Notes: What you talkin ‘bout Willis?

## Slide 119: BIOS Entry Vector Analysis: Short Cut 2
Follow the entry JMP
  Notice that IDA automagically modified our segment so it begins at seg:FE30
Manually touch up the FAR JMP same as before
We could optionally create a 32-bit segment here just to ensure it has a base of 0h
  Assume a flat memory model
Now we can go to the real BIOS initialization code entry, just like before!
This shortcut doesn’t always work
Notes: What you talkin ‘bout Willis?

## Slide 120: Lab: Scratch the surface
Repeat the process we just did for the E6400 BIOS on each of your BIOS dumps
We'll see if there are any where it leads to early confusion
Notes: http://www.walkwithgod.org/wp-content/uploads/2014/01/118-nails-on-a-chalkboard.jpg

## Slide 121: Memory Map

## Slide 122: Memory Map
One of the primary responsibilities of the BIOS is to program the memory map
Many devices, in order to be useful, require their interfaces be extended to memory
Also this is how the BIOS can ensure information about the way it set up the system is passed to the operating system at the time of handoff

## Slide 123: 4 “Basic” Ranges in System Memory
High Memory Range: Memory above 4GB (called Top of Upper Usable DRAM). Used for memory mapping and recoverable memory (system memory that overlaps with the PCI range)
  TOM (Top of Upper Memory): size of physical memory
PCI Memory Address Range: Used for memory-mapped IO (TPM, APIC, Flash, PCI Express, devices on chipset, etc.)
Main Memory Address Range: Addressable memory from TOLUD (Top of Low Usable DRAM) down to 1 MB
Compatible Memory space: 1 MB and below
TOUUD
TOLUD
TOM

## Slide 124: Memory Map
But on startup the processor is only aware of one memory range as we’ve seen
  Often called the Boot Block, it contains the entry vector and uncompressed BIOS code
The system automatically maps the top 16 MB of memory to the flash bios
  Non-negotiable, does not matter if your system has < 4 GB of memory, the system never actually accesses that memory. Rather, it is mapped to the flash device.
The rest of system memory needs to be configured by the BIOS
TOM
FFFF_0000

## Slide 125: Hardware Block Diagram
On the Mobile 4-Series Chipset, the BIOS (executed by the CPU), configures the MCHBAR in the DRAM Controller
FEDA_0000h (on an E6400 with 4GB RAM for example)
MCHBAR is now added to the memory map
So how does this actually occur?
FFFF_FFFFh
0000_0000h
FEDA_0000h
Offset | Name | Value
48h | MCHBAR | FEDA0000h
DRAM Controller | B0:D0:F0
Chipset
Offset | Name | Value
60h | PCIEXBAR | F8000000h
DRAM Controller | B0:D0:F0
F800_0000h

## Slide 126: Input/Output (I/O)
I/O, I/O, it’s off to work we go…

## Slide 127: 2 Types of I/O
Memory-Mapped I/O (MMIO)
Port-Mapped I/O (PMIO)
  Also called Isolated I/O
X86 systems employ both-types of I/O
Both methods map peripheral devices
Address space of each is accessed using instructions
  typically requires Ring 0 privileges
  Real-Addressing mode has no implementation of rings, so no privilege escalation needed
I/O ports can be mapped so that they appear in the I/O address space or the physical-memory address space (memory mapped I/O) or both
  Example: PCIExpress registers – both memory-mapped and port I/O
The I/O Controller Hub contains the registers that are located in both the I/O Address Space and the Memory-Mapped address space

## Slide 128: Memory-Mapped I/O
Devices can also be mapped to the physical address space instead of (or in addition to) the I/O address space
Even though it is a hardware device on the other end of that access request, you can operate on it like it's memory:
  Any of the processor’s instructions that reference memory can be used to access an I/O port located at a physical-memory address (MOV, for example)
  Operations like AND, OR, and TEST can be used on data at a memory-mapped address
Access byte, word, dword
The MOV instruction itself requires privileges only in protected mode based on the privilege level of the descriptor describing the segment

## Slide 129: Memory-Mapped I/O
For people not accustomed to working in low-level space, the term memory mapping can be a little confusing, mainly because of how the term is often used, for example:
“Device X is mapped to memory.”
I have noticed more than one person confused by this phrasing:
  Are it’s contents copied to memory? Or are memory accesses destined for that memory range redirected (decoded) to the device?
It’s the second one. Accesses destined to that memory range are decoded to the device
So now you know

## Slide 130
0000_0000h
0000_0001h
FFFF_FFFFh
.
.
.
.
.
.
.
.
.
MMIO Ports/Offsets
I/O Addresses
16-bit Offset 0
32-bit Offset 0
16-bit Offset 1
8-bit Offset 0
8-bit Offset 2
Offset 0
Offset 1
Offset 2
Offset 3
FED4_0000h
FED4_BFFFh
Memory-Mapped I/O
Sometimes you will see them referred to as “ports.” Most commonly they are referred to as offsets (like in the Intel datasheets)
For example:
Port 0 is located at offset 0 and can be accessed as a byte, word, or dword
.
.
.
.
.
.

## Slide 131: Memory Mapped IO
The colored regions are memory mapped devices
Accesses to these memory ranges are decoded to a device itself
Flash refers to the BIOS flash
APIC is the programmable interrupt controller
PCI Memory range is programmed by BIOS in the PCIEXBAR

## Slide 132: Peripherals that Map to Both
Devices can map to both memory and IO address space
PCI Express is a good example of devices that map to both the IO address space and the physical memory address space
Compatible PCI configuration space maps to IO Addresses CF8h and CFCh
Both Compatible PCI configuration space plus the extended header are also mapped to a memory location/size defined by the PCIEXBAR register located in the DRAM Controller
We'll get into this again once we get to PCI

## Slide 133: Port-mapped I/O Address Space
Software and hardware architectures of x86 architecture support a separate address space called “I/O Address Space”
  Separate from memory space
Access to this separate I/O space is handled through a set of I/O instructions
  IN,OUT, INS, OUTS
Access requires Ring0 privileges
  Access requirement does not apply to all operating modes (like Real-Mode)
The processor allows 64 KB+3 bytes to be addressed within the I/O space
Hearkens back to a time when memory was not so plentiful
You may never see port I/O when analyzing high-level applications, but in systems programming (and especially BIOS) you will see lots of port I/O
One of the biggest impediments to understanding what's going on in a BIOS
Port 0
Port 1
Port 2
Port 3
Port 4
Port 65535
0x0000
0x0001
0x0002
0x0003
0x0004
0xFFFF
.
.
.
I/O Address Space
.
.
.
Intel Programmer’s guide, Vol 1, 16.1

## Slide 134: Port I/O Accesses
Port I/O access are handled by the Controller Hub
  So in a chipset that has a Memory Controller Hub (MCH), the MCH performs no translation of accesses to I/O space
  The MCH just forwards them to DMI (and thus to the I/O Controller Hub)
The Controller Hub (ICH/PCH) contains the registers that are located in the I/O address space
Again, separate and distinct from physical memory address space
Intel Programmer’s guide, Vol 1, 16.1
I/O
Space
0xFFFF
0x0000

## Slide 135: How does the hardware distinguish between port IO and memory access?
Intel 8088 chip
(from the bad old days)
http://www.cpu-world.com/info/Pinouts/8088.html
There's a bit for that!
Notes: http://www.cpu-world.com/info/Pinouts/8088.html
http://static2.businessinsider.com/image/4ad73b48000000000004e48d/steve-jobs-pointing-apple.jpg

## Slide 136: I/O Mapped Address Space
I/O Address space consists of two ranges or types of access:
Fixed
  Addresses/peripherals cannot be relocated
  In some instances they can be disabled, but not all
Variable
  These addresses can be relocated
  Can also be disabled
Addressable size can be 8 bits, 16 bits, or 32 bits

## Slide 137: 1. Fixed I/O Ports
The addresses depend on the implementation of the I/O Controller Hub present in your system
  Check the I/O Controller Hub Datasheet to make sure you are interpreting these signals properly
Address ranges that are not listed or marked “Reserved” are not decoded by the ICH
  Unless one of the variable ranges has been relocated to that address
Each fixed IO address is a 2-byte word
Remember, on the “other side” of each port address/range there is a hardware device
  Device interaction and behavior will differ between devices
  This is why it can be difficult to decipher when analyzing
Port I/O is a gateway to a black box
Intel, Vol 1, 16.1

## Slide 138: Example: ICH 9 Fixed Range

## Slide 139
Port 60 is the historic location of the 8042 keyboard controller status/command port. And port 64 is the data port. Notice how it doesn't tell you that, it just says they're being forwarded on to LCP. Annoying for trying to figure out what's being talked to

## Slide 140
Takeaway: there’s a lot of fixed IO address space, and it’s fragmented too. This is why it’s recommended that devices map their interfaces to memory rather than IO address space
This one we’ll
talk about
explicitly later

## Slide 141: 2. Variable I/O Ports
Can be relocated to another address
Can be set/disabled using Base Address Registers (BARs) or configuration bits in the various PCI configuration spaces
  Which we shall discuss very soon!
The BIOS (and/or other PCI devices or ACPI) can adjust these values
  Actually pretty much any privileged app can…
The same as the fixed range, on the “other side” of each port address/range there is a peripheral device
  Device interaction and behavior will differ between devices
ICH does not check for overlap
  Results “unpredictable” if overlapping
Intel, Vol 1, 16.1

## Slide 142: Example: ICH 9 Variable IO Range

## Slide 143: IN - Input from Port
Note it's DX, not DL. That means the DX form can specify all 2^16 ports, but the IMM8 form can only specify 2^8 ports.
“When accessing a 16- and 32-bit I/O port, the operand-size attribute determines the port size.” (Because as usual there's an overloaded opcode for 16/32 bit form)
  Remember if you're in a 16 bit segment it's 16 bit, if you're in a 32 bit segment it's 32 bit. But you can override it with an operand size instruction prefix which is talked about later.

## Slide 144: OUT - Output to Port
Basically the same caveat as IN

## Slide 145: Port IO Assembly Examples (showing that you can either use an 8 bit immediate or a 16 bit register (dx) to specify port)
Read from port 0xB3:
Write 0x1234 to port 0xB2:
MOV AL, 0x1234
OUT 0xB2, AL
MOV AL, 0x1234
MOV DX, 0xB2
OUT DX, AL
MOV DX, 0x70
OUT DX, 0x05
MOV DX, 0x71
IN AL, DX
IN AL, 0xB3
Index/Data pair read offset 0x05:
MOV AL, 0x05
MOV DX, 0x70
OUT DX, AL
MOV DX, 0x71
IN AL, DX
MOV DX, 0x70
OUT DX, 0x05
MOV DX, 0x71
OUT DX, 0x10
Index/Data pair write to offset 0x05:
MOV AL, 0x05
MOV DX, 0x70
OUT DX, AL
MOV DX, 0x71
MOV AL, 0x10
OUT DX, AL
Notes: You should use cli, sti to clear/set interrupts prior to doing these reads/writes
Also technically you should go through the controller to avoid race conditions

## Slide 146: Port IO
CPU
CLI
MOV AX, PORT
OUT AX, VAL
STI
VAL could be a command or data (interpreted by the device)
It is not necessarily known what the black box on the end of a port does
Check your Controller Hub datasheet and/or the LPC decode registers (might offer clues)
CPU
CLI
MOV AX, PORT
IN AX, VAL
STI
Black Box
Black Box

## Slide 147: Port IO Index/Data Pair
Black Box
CPU
Some devices use an index/data pair for IO
An offset is written to the index port
Next a value is read from or written to that offset from the Data port
Devices such as this are CMOS, PCI (all), and the Keyboard Controller on the E6400
  http://esec-lab.sogeti.com/dotclear/public/publications/11-recon-stickyfingers_slides.pdf
CLI
MOV DX, 0x70
OUT DX, 0x04
MOV DX, 0x71
IN AL, DX
STI

## Slide 148: Identifying Port I/O
First try deciphering port IO devices by using the datasheets (Controller Hub either ICH or PCH)
OS Dev
  http://wiki.osdev.org/I/O_Ports (which links you to...)
Boch’s or Ralf’s
  http://bochs.sourceforge.net/techspec/PORTS.LST
  Last change was in 11/6/94 and that’s just how it is with most BIOS information
Vendors can extend a device interface to any unoccupied IO address

## Slide 149: Example: Port IO Configuring PCIEXBAR
On the Mobile 4-Series Chipset, the BIOS (executed by the CPU), configures the PCIEXBAR in the DRAM Controller
F800_0000h (on an E6400 with 4GB RAM for example)
PCI Memory range is now mapped
So how does this configuration actually occur? PCI…
Chipset
Offset | Name | Value
60h | PCIEXBAR | F8000001h
DRAM Controller | B0:D0:F0
F800_0000h
Notes: As previous, this logical diagram shows the connection between the CPU and the rest of the system. The CPU is connected directly to the Chipset northbridge.

## Slide 150: PCI (and PCI Express)
All your base. base. base…
all your base address register are belong to PCI

## Slide 151: PCI
Peripheral Component Interconnect (PCI)
  Also called Compatible PCI
It’s a Bus protocol developed by Intel around 1993
Purpose is to attach/interconnect local hardware devices to a computer
PCI is integrated into the chipset, forming a “backbone”
  Holds true for both Intel and AMD-based systems
  Logically speaking, the Chipset is a PCI System
32-bit bus with multiplexed address and data lines
  Supports 64-bit by performing two 32-bit reads
PCI component interface is processor independent
  The CPU/BIOS reads and writes to the configuration space to configure much of the system
Intel’s MCH/ICH chipsets implement PCI Local Bus Protocol 2.3
PCH chipsets implement PCI Express protocol (v. 2.0)
  Still supports PCI 2.3
PCI standards are currently maintained and defined by the PCI /SIG:
  http://www.pcisig.com/specifications/
Notes: First we’ll talk about Compatible PCI, then we’ll cover PCI Express afterwards. Once you know PCI, PCI Express is just a logical extension with a few key differences.
You can call them “PCI systems” and not really be wrong to do so, at least logically. Although a hardware-guy might get mad but will concede your point if you specify logically.

## Slide 152: Generic PCI Topology: Buses, Devices, and Functions
Up to 256 Buses
Each Bus can have up to 32 devices attached
Each Device can extend up to 8 Functions
Buses are interconnected by Bridges
Multiple bridges can be connected through a bridge interface and are enumerated

## Slide 153: PCI Address Spaces
PCI implements three address spaces:
1) PCI Configuration Space
  Required/standard. Defined in the specifications. Every PCI device has a configuration space.
2) PCI Memory space
  Optional. Dependent on whether the device manufacturer needs to map system memory to the PCI device
3) PCI I/O space
  Optional. Same as PCI Memory Space
Notes: Ok so now the good stuff. How does the software block diagram help us out?

## Slide 154: PCI Express (PCIe)
Peripheral Component Interconnect Express (PCIe)
Developed around 2004 (not just by Intel but a collective)
Packet-based transaction protocol
Very different from PCI at the hardware level
For software configuration purposes, it is mostly the same
  Adds an extended configuration space of 4KB
Provides backwards compatibility for Compatible PCI
Adds 4KB of PCI Express Extended Capabilities registers
  Located in either the Configuration space starting at offset 256 (immediately following the Compatible PCI configuration space)
  Or located in the Root Complex Register Block (RCRB)
We’ll cover the Extended Capabilities at the end separate from all else since its PCIe specific
Notes: First we’ll talk about Compatible PCI, then we’ll cover PCI Express afterwards. Once you know PCI, PCI Express is just a logical extension with a few key differences.
You can call them “PCI systems” and not really be wrong to do so, at least logically. Although a hardware-guy might get mad but will concede your point if you specify logically.

## Slide 155: Generic PCIe Topology:
The Root Complex connects the processor to the system memory and components
Same number of devices supported as PCI
  Provides 4KB worth of Extended Capabilities register space to each Function
Up to 256 PCIe buses
Up to 32 PCIe devices
Up to 8 Functions
Each Function can implement up to 4 KB of configuration space

## Slide 156: Mobile 4-Series Chipset PCIe Topology
Example:
The GMCH on the 4-Series Chipset is part of a Root Complex that connects the CPU to the graphics devices and the IO Controller Hub
Contains 2 RCRBs (Root Complex Register Blocks)
  Device configuration space, each is 4 KB, similar to configuration space
Mobile 4-Series Chipset datasheet
Root Complex
Cheers!

## Slide 157: Not really a “pure” PCI/PCIe Implementation
Chipset logical Bus 0 is highlighted
Direct Media Interface(DMI) is not PCI so from a hardware perspective, the Chipset is not entirely PCI
Logically, however, it is considered to be PCI and is configured as such
If a device (graphics card) were to be plugged into Host-PCI Express Bridge, it would be on a Bus other than 0
  According to documentation, the BIOS chooses the Bus number
Mobile 4-Series Chipset datasheet

## Slide 158: PCI Express Address Spaces
PCI Express implements four address spaces:
1) PCIe Configuration Space
  Required/standard. Defined in the specifications. Every PCIe device has its configuration space mapped to memory.
  Also provides the first 256 bytes of compatible PCI (memory-mapped and via port IO for backwards compatibility)
2) PCIe Memory space
  Optional. Dependent on whether the device manufacturer needs to map system memory to the PCI device
3) PCIe I/O space
  Optional.
4) PCIe Message Space
  For low-level protocol messaging/interrupts. These are now sent via this address space rather than a physical side-channel
Notes: Ok so now the good stuff. How does the software block diagram help us out?

## Slide 159: Configuration Space Accesses
There are two ways to access the compatible PCI configuration space registers (0 to 255) but only one way to access the extended configuration space offered by PCI Express (255 to 4KB)
  I/O Mapped Address Space
  Memory-Mapped Address Space
Generally speaking, you will see accesses to PCI being performed via I/O in a couple situations:
  When in Real Mode when accesses to 32-bit memory space is limited
    Real Mode may be re-entered even after the system has transitioned to Protected mode (up to the vendor and their implementation, flat real mode could pull it off)
    I have only seen this done in a Legacy BIOS, never in UEFI
  Before PCIEXBAR has been configured
Outside of those situations, you’ll probably see PCI accesses performed via memory-mapped I/O
But of course this is all up to the developers; it’s not a law of physics

## Slide 160: Compatible PCI Configuration Space
This refers to the software generation of PCI configuration transactions
  those generated by the CPU/BIOS
Compatible PCI extends 256 bytes of Configuration address space to the CPU/BIOS
CPU/BIOS programs the registers contained therein to configure the device and system parameters
Compatible PCI is configured using the port I/O address/data pair (CONFIG_ADDRESS, CONFIG_DATA)
Two 32-bit I/O locations are used to generate configuration transactions
  CF8h (CONFIG_ADDRESS)
  CFCh (CONFIG_DATA)
Curiously, these are never listed in the Fixed IO Address space registers in the applicable chipset datasheets, but are explicitly mentioned as CF8/CFC in the datasheets

## Slide 161: I/O Port CONFIG_ADDRESS (CF8h)
32 bits
Port CF8h
Bit 31 when set, all reads and writes to CONFIG_DATA are PCI Configuration transactions
Bits 30:24 are read-only and must return 0 when read
Bits 23:16 select a specific Bus in the system (up to 256 buses)
Bits 15:11 specify a Device on the given Bus (up to 32 devices)
Bits 10:8 Specify the function of a device (up to 8 devices)
Bits 7:0 Select an offset within the Configuration Space (256 bytes max, DWORD-aligned as bits 1:0 are hard-coded 0)
Addresses are often given in B(us)/D(evice)/F(unction), Offset notation
Notes: Bits 1:0 ensure 4-byte aligned addresses

## Slide 162: Compatible PCI Configuration Registers
256 bytes
Every PCI device implements this space
  PCI Express further extends this to 4KB, we’ll cover that in a bit
First 0x40 bytes are the header
The remaining bytes consist of a device dependent region, which consists of device-specific information per PCI SIG documentation
Type 0 header, General PCI Device, PCI Spec 2.3
PCI Configuration Registers Header
00h
3Ch
FCh
Device Dependent Region
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth

## Slide 163: PCI Configuration Registers Header (aka "configuration space all up in your face!")
This is what you should visualize when we're talking about access to specific register number offsets in CONFIG_ADDRESS
Type 0 header, General PCI Device, PCI Spec 2.3
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth

## Slide 164: I/O Port CONFIG_DATA (CFCh)
CONFIG_DATA can be accessed in DWORD, WORD, or BYTE configurations
Reads and Writes to CONFIG_DATA with Bit 31 in CONFIG_ADDRESS set/enabled results in a PCI Configuration transaction to the device specified in CONFIG_ADDRESS
PCI Spec says that if Bit 31 is not enabled, then the transaction is forwarded out as Port I/O

## Slide 165: BIOS Analysis: Finding PCI Configuration
Scenario: Let’s say we want to locate where in the executable BIOS the system programs the PCIEXBAR (determines where in the PCI Express Register Range will be mapped in memory
Looking in our datasheet, we see that, on our sample system, it is located in the DRAM Controller, which is located at B0:D0:F0. The specific 64 bit register is then at offset 60-67h
So we know I/O accesses to this will be to 0x80000060
  Remember, accesses to CONFIG_ADDRESS are always 4-byte aligned
It’s not elegant, but it is scriptable
Notes: This is my least favorite way of finding where things are configured, but it *can* work

## Slide 166: BIOS Analysis: Finding PCI Configuration
So with 80000060h in mind, let’s look at our BIOS binary which we dumped using Copernicus
Looking in IDA Pro (Free version works fine), we can go to Search -> sequence of bytes, and enter: 60 00 00 80
  Little endian byte order
Simplistic, perhaps even lame, yet yields useful results:
Notes: We’ve either already mentioned these tools or will talk about them in more detail.

## Slide 167: BIOS Analysis: Interpreting PCI Configuration
For example the following disassembly snapshot maps the PCI Express registers to memory address F800_0000h
Per the PCIEXBAR register definition in the datasheet, it also allocates 64MB of space for it in the memory map (bits 2:1) and then activates it (bit 0)
  So interestingly not all devices/functions may be mapped to memory
System configuration is very concise!
F800_0000h
FC00_0000h
PCI Express
configuration space
Notes: Look at all that is done in just a few instructions. BIOS is very concise code indeed

## Slide 168: Back to that Memory Map…
Looking for 80000060h led us to a big ol’ block of memory map configuration code
I’ll leave it up to you to verify, but this block (in order):
Sets the Egress Port Base Address to FEDA_5000h and enables it
Sets the MCH Memory Mapped Register Range Base to FEDA_0000h and enables it
Allocates 64MB of memory for PCIEXBAR at base address F800_0000h
Sets DMIBAR to FEDA_4000h and enables it
And lastly it’s testing bit 49 (not a typo) in the Capabilities register to check whether the MCH is capable of supporting DDR SDRAM
You will find a lot more in the BIOS, but this is how its done
Notes: Some things are easier to look at in text mode than graph mode (in my opinion) and this is one of them.
So this sets up a whole bunch of that memory map, which pretty much brings us full circle.
Some of these you’ll really have to look up for yourself. DMIBAR, etc.

## Slide 169: Lab: Use RW-E to Read PCI
For example, in the Intel datasheet, let’s find the RCRB address since we’ll be using it often, e.g. to get to the SPI flash interface
  Refer to your datasheet if doing on your own system but it should be at B0:D31:F0 (LPC device), offset F0h
If the bus isn't specified by the Intel data sheet you can safely assume it's bus 0
This association is highly refreshing!
Notes: "RCBA = mirror universe spock, because it's the mirror of the ABCs. RCRB = RC Cola…because I wanted one of them to be RC Cola."
Key thing to remember: "RCBA holds RCRB"
http://img1.wikia.nocookie.net/__cb20090608054928/memory-gamma/images/a/a7/Spock_(mirror).jpg
http://ecx.images-amazon.com/images/I/41SH8i1ZunL.jpg
http://2.bp.blogspot.com/-78xSvq-r1ec/UPLWVmmR8kI/AAAAAAAABcw/Icea0Nvo_HQ/s1600/Spock+Goatee.tiff

## Slide 170: Find Root Complex Register Block (method 1)
RCBA register (LPC D0:F31, offset F0h) holds RCRB address
It serves as a base address for memory mapped BARs such as the MCHBAR and SPIBAR (will be identified/explained as they come)
On our Dell E6400 with 4GB RAM, RCRB is at FED1_8000h

## Slide 171: Find Root Complex Register Block (method 2)
CF8h and CFCh are adjacent dwords
LPC (B0:F31:D0, offset F0h) is 8000F8F0
So enter 8000F8F0 into port CF8h
CFCh

## Slide 172: Find Root Complex Register Block (method 2, cont)
So we have now determined that the RCRB address is FED1_8000h
  Bit 0 is just an enable bit, still a 32-bit physical address
Aside, the dword at CF8h resets itself. If you keep this IO window open you might see PCI port IO accesses (if there are processes running that perform this)
  I have seen this occur on Windows 8 where the vendor/device ID of one of the PCI devices on the CPU is read every few seconds or so; I have not determined which process(es) are doing this
CFCh
Notes: "And so when you put RCRB into CF8, out 'pops' (hyuk hyuk) RCBA!"
(it's a joke because in the US midwest we call soda pop just "pop")

## Slide 173: Compatible PCI Configuration Registers
Implemented in PCIe too
PCI Configuration register
256 bytes
Every PCI device implements this space
  PCI Express further extends this to 4KB, we’ll cover that in a bit
First 0x40 bytes are the header
The remaining bytes consist of a device dependent region, which consists of device-specific information per PCI SIG documentation
Type 0 header, General PCI Device, PCI Spec 2.3
PCI Configuration Register Header
00h
3Ch
FCh
Device Dependent Region
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth
  ??

## Slide 174: PCI Configuration Registers Header (aka "configuration space all up in your face!")
Implemented in PCIe too
Three header types (0-2)
Type 0 = General Device
Type 1 = PCI-to-PCI Bridge
Type 2 = CardBus Bridge
Shown is Type 0
Divided into 2 parts:
First 16 bytes (0-F) are standard and defined the same for all devices
The remaining header bytes are optional per the vendor, depending on what function the device performs
Type 0 header, General PCI Device, PCI Spec 2.3
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth

## Slide 175: PCI Device Identification
Five fields (all required) can be used to identify the device and its basic functionality
Vendor ID identifies the manufacturer of the device
  Allocated by the PCI SIG to ensure each is unique
Device ID identifies the particular device, set by the vendor
Revision ID is set by the vendor, viewed as an extension to Device ID (Intel is 8086h, AMD microcontrollers is 1022h)
Class Code used to identify the generic functionality of the device
Header Type identifies what type of header to expect (per the previous slide, general, PCI bridge, CardBus bridge)
  Bit 7 being set (0x80) indicates device is a multi-function device
Type 0 header, PCI Spec 2.3
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth

## Slide 176: Base Address Registers (BARs)
Base Address Registers point to the location in the system address space where the PCI device will be located
  The device RAM, etc. (anything really, per the vendor)
BARs are R/W and the BIOS programs them to set up the Memory Map
PCI Configuration Register provides space for up to 6 BARs (bytes 10h thru 27h)
  BAR[0-5]
Each BAR is 32-bits wide to support 32-bit address space locations
Concatenating two 32-bit BARs provides 64-bit addressing capability
Type 0 header
Notes:   If B0:D0:F0 Header type & 0x80 then it’s a multi-controller device
  F0 will control Bus 0
  F1 will control bus 1 and so forth

## Slide 177: Base Address Register for Memory Space
Actual Base address is obtained by logically ANDing the value in bits 31:4 with FFFF_FFF0h (mask the low 4 bits)
  Actual Base Address = (BAR[x] & FFFF_FFF0h)
A cleared Bit 0 indicates this will be located in memory address space, otherwise IO space
64-bit accessibility is provided by programming back-to-back BARs
  (BAR[x] & FFFF_FFF0h) + (BAR[x+1] & FFFF_FFF0h)*
*OSDEV: http://wiki.osdev.org/PCI

## Slide 178: Base Address Register for I/O Space
Actual Base address is obtained by logically ANDing the value in bits 31:4 with FFFF_FFF0h (mask the low 4 bits)
  Actual Base Address = (Base Address[31:2] & FFFF_FFFCh)
If Bit 0 is 1, then the Base Address will be an offset in the port I/O address space
PCI SIG recommends that devices are mapped to memory rather than I/O, because I/O can be fragmented
  Look at the Fixed and Re-locatable I/O ports in your friendly neighborhood ICH (or PCH) datasheet

## Slide 179: BAR Limit/Size
A Base Address is half the information that’s needed
We need a limit to determine how this PCI device will be mapped into memory
How does the BIOS determine how much space the device needs?
?
Base Address = (E000_0000h & FFFF_FFFFh)

## Slide 180: BAR Space Utilization (Size)
CPU/BIOS can write all 1’s to the BAR to determine how much address space the device needs by writing all 1’s to the BAR
Device will return 0’s in all "I don’t care if they're set" bits
  Or put another way, returns 1s in all the "don't set" bits
Pro tip: save the original value first! ;)
The device returns the don’t care bits into the BAR thus telling you how much address space the device needs
1111 1111 1111 1111 1111 1111 1111 1111
1111 1111 1111 0000 0000 0000 0000 0000
Example
return
FFFF_FFFFh
FFF0_0000h
Notes: How might it know that writing 1s is meant to check size? Maybe because if you write a 1 into bit 0, then bit 1 is reserved to 0, and thus writing a 1 into that reserved bit means its size checking time. Maybe test with a less-than-all-1s example

## Slide 181: Ex 1: Determine Device Address Space Size
The IEEE 1394 FireWire device on the E6400 has a BAR located at F1BFF800h (lower bits are already 0 so this is the actual base address in memory)
  Bit 0 = 0, so it’s mapped to memory
  Bits 2:1 = 00 so it’s 32-bit address space (below 4GB)
  Bit 4 = 0, so it’s not pre-fetchable
We can open up a memory window at F1BFF800h and see the device

## Slide 182: Ex 1: Determine Device Address Space Size
We write all 1’s to it just like the BIOS does to determine the size of the FireWire device
When you try this for yourself, try to pick a device that you know is not actively being used. ;)
  These things tend to not fail gracefully in my experience
  But it’s nothing a reboot shouldn’t fix (but still, you have been warned, there is no guarantee the vendor has protected itself adequately from erroneous writes)
  Check the devices datasheet you might find something interesting

## Slide 183: Ex 1: Determine Device Address Space Size
The device returns the value FFFF_F800h to the BAR
  These are the don’t care bits which tell us the range of the device memory
  ~(FFFF_F800) = 7FFh, so the device’s mapped address range in memory is F1BF_F800h - (F1BF_F800 + 7FFh)
Also notice that when we change the value in the BAR, the device is no longer mapped to F1BF_F800h (as evident by all 0xFF’s)

## Slide 184: Ex 1: Determine Device Address Space Size
So let’s verify our mapped range:
We’ll view memory address F1BF_FF80h which is 80h bytes before our upper limit address as denoted by the red line

## Slide 185: Ex 1: Determine Device Address Space Size
When we reset the BAR back to its original value (F1BF_F800h), the device is (re)mapped back to memory
And it shows our upper limit measurement was correct
It’s good to see for yourself how this world works

## Slide 186: Ex 2: Relocate the PCI Device Mapping
So as you noticed, when we changed the value in the BAR, the device was no longer mapped to memory
We wrote a value of all 1’s to it which is an invalid base address in itself (but is designed to return the mask)
So what if we write a valid* address for the device to be mapped to?
*Overlapping ranges are not checked for, “valid” means proceed at your own risk

## Slide 187: Ex 2: Relocate the PCI Device Mapping
Let’s try moving this to F1BF_F000h
  On the E6400 I checked beforehand and saw that this address space appeared to be unused (was all 0xFF’s)
When we write F1BF_F000h to the BAR… the device has been relocated.
This is part of the way the CPU/BIOS builds the memory map
  And you can too, with sufficient permissions
  Not really a security issue, just a “how the world works” kind of example

## Slide 188: Things to be aware of once you start learning down at this level
Here's a recent ASIA CCS paper evaluating whether past work on attacks that manipulate PCI (e.g. forcing MMIO overlap, configuration range overlap, etc) and other low level information for a pass-through device inside virtual environments (answer: doesn't seem like it, but they found a new attack :))
On the Feasibility of Software Attacks on Commodity Virtual Machine Monitors via Direct Device Assignment – Pek et al.
https://www.iseclab.org/people/andrew/download/asia14.pdf

## Slide 189: Command Register and Address Space Access
Determine whether a PCI device will respond to I/O accesses and Memory-Space accesses
The BIOS must set the applicable bit(s) to 1 if the device will be mapped to memory and/or I/O space
Turning these off/on will un/map the device (BARs) in the address space
Notes: Basically think of it as the PCI device has some default state, e.g. telling you whether it is 32 or 64 bit, whether it is prefetchable, whether it wants to map something into memory or IO, etc. The BIOS then comes along and saves this information, queries the mapping size by doing the write-1s, and then maps it wherever it wants to, and sets the appropriate command bits

## Slide 190: BAR Summary in relation to BIOS
E000_0000h
E800_0000h
BIOS
Memory Map
As discussed above, PCI device address space is added to the memory map by the BIOS during the boot process
They can be relocated as necessary by the system software
Same principle if mapped to I/O address space instead of memory

## Slide 191: PCI/PCIe Expansion ROMs (XROMs)
A PCI/PCIe Expansion ROM is executable code located on a PCI device
Not every device will have one
  Graphics cards, network cards will likely have one
  A device can have multiple XROMs (for multiple architectures)
Benign or otherwise this code gets executed by the CPU/BIOS during the boot process
Good references:
  https://sites.google.com/site/pinczakko/building-a-kernel-in-pci-expansion-rom (Darmawan Salihun)
  http://www.blackhat.com/presentations/bh-dc-07/Heasman/Paper/bh-dc-07-Heasman-WP.pdf (John Heasman)
  http://pacsec.jp/psj13/psj2013-day2_Pierre_pacsec-uefi-pci.pdf (Pierre Chifflier)
Logically speaking, they are handled the same on PCI Express as they are in PCI
They are configured via a separate BAR called the Expansion ROM Base Address Register

## Slide 192: Expansion ROMs (aka: Option ROMs)
XROMs have their own BAR called the Expansion ROM Base Address Register
  On general type PCI devices it’s located at offset 30h
  On bridge type devices it’s at 38h
BIOS initializes the XROM BAR like the other BARs, but hands off execution control to the code it points to
XROMs are copied to memory before being executed
  On legacy systems they are copied to C0000 to DFFFFh range
The XROM BAR operates similarly to the other BARs but the decoding is different
Notes: *** UEFI XROM location

## Slide 193: Expansion ROM Base Address Register
The LSB determines whether accesses to the Expansion ROM are permitted. When asserted to 1, they are permitted
Even when a device has an Expansion ROM, its BAR may still be 0 (meaning access to it is not permitted)
Like the PCI BARs, the Expansion ROM BAR is also R/W
An expansion ROM will only respond to accesses if the memory space bit in the Command Register and the Expansion ROM Enable bit are both set
The CPU/BIOS handles Expansion ROMs a little differently depending on whether they are add-on cards or built-in to the mainboard

## Slide 194: How CPU/BIOS Discovers XROMs
To determine whether the device has implemented an Expansion ROM base:
All 1’s are written to the top 21 bits (31:11) of the Expansion ROM BAR
If the device returns anything other than 0, then it has implemented an Expansion ROM
0
CPU/BIOS writes FFFF_F800h
1111 1111 1111 1111 1111 1
Expansion ROM Base Address Register
Notes: I have seen it written that 1’s are written to all bits except bit 0. I know I read it but can’t cite the source.
I’ve tried it both ways and get the same output either way. I choose the above way since this is how the Linux kernel does it (PCI_ROM_ADDRESS_MASK = ~7FFUL)

## Slide 195: How CPU/BIOS Discovers XROMs
The return address indicates both the size of the ROM and the memory alignment (mask) required by the ROM:
Per the above example:
Size = ~FFFE_0000 +1 = 2_0000h bytes
ROM must be mapped to a 128KB-aligned memory address
0
Device returns FFFE_0000h
1111 1111 1111 1110 0000 0
Expansion ROM Base Address Register
Notes: I have seen it written that 1’s are written to all bits except bit 0. I know I read it but can’t cite the source.
I’ve tried it both ways and get the same output either way. I choose the above way since this is how the Linux kernel does it (PCI_ROM_ADDRESS_MASK = ~7FFUL)

## Slide 196: How CPU/BIOS Discovers XROMs
Next the CPU/BIOS maps the ROM to an unused portion of memory
Then it sets the enable bit so that the ROM is now accessible at the address defined by the BIOS
1
CPU/BIOS maps the ROM and enables it
( Some memory address )
Expansion ROM Base Address Register
Notes: I have seen it written that 1’s are written to all bits except bit 0. I know I read it but can’t cite the source.
I’ve tried it both ways and get the same output either way. I choose the above way since this is how the Linux kernel does it (PCI_ROM_ADDRESS_MASK = ~7FFUL)

## Slide 197: How CPU/BIOS Discovers XROMs
If anything other than the “AA55” signature is present, there is actually no Option ROM provided by the device, despite the fact that it returns a mask as if there were
  I have some ice cream. Want a lick? Psych!
There may still be an option ROM, however, some companies implement them in non-standard ways
CPU/BIOS checks memory for Option ROM structure
PCI Express Revision 3.0
Notes: I have seen it written that 1’s are written to all bits except bit 0. I know I read it but can’t cite the source.
I’ve tried it both ways and get the same output either way. I choose the above way since this is how the Linux kernel does it (PCI_ROM_ADDRESS_MASK = ~7FFUL)

## Slide 198: CPU/BIOS Expansion ROM Discovery
A PCI device can share a decoder between the Expansion ROM BAR and other BARs
For example:
Some vendors mirror their Expansion ROMs at BAR[n] or at an offset from BAR[n]
  NVidia sometimes puts them at BAR[0] + 30_0000h (per the developers of Flashrom )
  http://flashrom.org/Flashrom
It is possible that there simply is no Expansion ROM present on the device
  Could be located in a compressed module in the BIOS binary
Notes: This whole process is wonky. The nVidia graphics XROM is at EFFE_0000h and there is NO rhyme or reason as to why that is (at least not per the PCI spec)
Writing FFFFF800 to the XROM BAR returns FFFE_0000h. So close… what’s the connection???

## Slide 199: Expansion ROM Discovery: User Example (Same as BIOS)
This example pertains to the nVidia VGA card on the E6400 laptop
Verify that the memory-enable space bit 1 in the command register (offset 04h) is asserted
Writing FFFF_F800h to offset 30h returns FFFE_0000h indicating that an Expansion ROM [might be] present
  Bit 17 is the LSB, which indicates a 128KB ROM
  Size = ~FFFE_0000 + 1 = 2_0000h bytes

## Slide 200: Expansion ROM Discovery: User Example (Same as BIOS)
We (or the BIOS) should be able to choose a memory address for the ROM to be mapped to
Address must meet alignment requirements
Address must provide enough room for the XROM
Must enable the XROM decoding (assert bit 0, enable)
00100001

## Slide 201: Expansion ROM Discovery: User Example (Same as BIOS)
If there is anything other than the “AA55” XROM signature, then there is actually no option ROM present
As it turns out, in this case, there is no option ROM located on the device
This option ROM is located on the BIOS flash as a compressed module
00100001

## Slide 202: Expansion ROM Hacking
Hacking an Expansion ROM typically requires re-flashing the firmware on the device
  Sometimes the “RO” in ROM is a bit of a misnomer as we shall see in the latter topics of the class
  Although in the case we just saw, modifying the BIOS itself could permit an attacker to insert a malicious XROM
If a vendor offers a utility to update the flash then you know the flash is writeable
Good reference on XROM hacking:
http://resources.infosecinstitute.com/pci-expansion-rom/
It’s important for Option ROMs to be measured (measured boot) before being executed
  Captain obvious here

## Slide 203: PCIe Extended Configuration Space
If a device is PCIe, the extended capabilities registers always start immediately following the compatible PCI configuration space (at 100h)
If device is PCIe but does not implement capabilities, the header contents must be all 0’s (unless it’s in the RCRB in which case Capability ID is FFFFh; but all others 0)
PCI Express 3.0 Spec
Extended capabilities header

## Slide 204: PCIe Address Mapping (PCIEXBAR)
PCIEXBAR (D0:F0, Offset 60-67h) points to the memory location where the PCIe configuration space is mapped
Legacy compatibility space
for D0:F0 (PCI device). Space extends to FFFh but is all 0xFF’s

## Slide 205: PCIe XROMs
Expansion ROMs are handled the same in PCI Express for backwards compatibility
Also, they are handled the same in a UEFI BIOS, since UEFI isn't re-defining PCI
  If UEFI secure boot is enabled, the Option ROMs will either have their signatures verified prior to being loaded and executed or possibly just not be allowed to be loaded
  Also, whereas there can be more than one option ROM on a device (to support different architectures), on a UEFI device a single option ROM could be implemented in UEFI byte code for use on any UEFI system)